August 2, 2007

REVISION OF SECTION 105

FAILURE TO MAINTAIN ROADWAY OR STRUCTURE

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in projects having traffic signals.  The designer will specify on the General Notes whether the roadway is classified as urban or rural.  The Contractor shall have 1 hour to respond to urban roadways and 4 hours to respond to rural roadways for traffic signal maintenance.

August 2, 2007

REVISION OF SECTION 105

FAILURE TO MAINTAIN ROADWAY OR STRUCTURE

Section 105 of the Standard Specifications is hereby revised for this project as follows:

Delete subsection 105.19 and replace with the following:

105.19 Failure to Maintain Roadway or Structure.  If the Contractor fails to comply with the provisions of subsection 105.18, the Engineer will immediately notify the Contractor of such noncompliance. Except in the case of traffic signal maintenance, the Contractor shall respond and remedy unsatisfactory maintenance within 24 hours after receipt of such notice.  If the Contractor fails to remedy unsatisfactory maintenance in the allotted time, the Engineer may immediately proceed to maintain the project, and the entire cost of this maintenance will be deducted from the monies due or to become due to the Contractor on the Contract.

In the case of traffic signal maintenance, the Contractor shall respond and remedy unsatisfactory maintenance within one hour of receipt of notice on urban highways, and within four hours of receipt of notice on rural highways.

Traffic signal maintenance shall include all approved traffic control items and work that are required to maintain traffic through the affected area while the traffic signal is being repaired or replaced.  If the Department performs traffic signal maintenance, the Department shall be held harmless for all subsequent occurrences of maintenance to the signals that the Department maintained.