April 12, 2007

REVISION OF SECTION 214

LANDSCAPE ESTABLISHMENT

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in projects having landscape establishment.

April 12, 2007

REVISION OF SECTION 214

LANDSCAPE ESTABLISHMENT

Section 214 of the Standard Specifications is hereby revised for this project as follows:

Subsection 214.04 shall include the following:

The beginning of the Landscape Establishment period depends upon receipt of the written “Notice of Substantial Landscape Completion” from the Engineer. Substantial Landscape Completion occurs when all plant materials in the Contract have been planted and all work under Sections 212, 213, 214 and 623 has been performed, except for the Section 214 pay item, Landscape Maintenance.  If the Notice of Substantial Landscape Completion is issued during the spring planting season, the Landscape Establishment period begins immediately and lasts for a period of 12 months.  If the Notice of Substantial Landscape Completion is issued at any other time, the Landscape Establishment period begins at the start of the next spring planting season and lasts for a period of 12 months.

In subsection 214.04(a) delete the second paragraph and replace it with the following:

Dead, dying or rejected material shall be removed each month during the Landscape Establishment period as directed.  Plant replacement shall be performed during the spring planting seasons at the beginning and end of the Landscape Establishment Period.  Plant replacement stock shall be planted in accordance with the Contract and is subject to all requirements specified for the original material.  Plant replacement shall be at the Contractor’s expense.

Section 214.04(b) shall include the following:

During the landscape establishment period, the Contractor shall water, cultivate, and prune the plants and repair, replace, or readjust guy material, stakes, and posts as required or directed by the Engineer.  The Contractor shall reshape plant saucers, repair washouts and gullies, replace lost wood chip mulch, keep all planting sites free from weeds and do other work necessary to maintain the plants in a healthy and vigorous growing condition.  This includes seasonal spraying or deep root watering with approved insecticides or fungicides as required.