April 11, 2008

REVISION OF SECTION 411

EMULSIFIED ASPHALT

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by the Standards and Specifications Unit of the Project Development Branch.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on projects having emulsified asphalt used for seal coat and fog coat in chip seals.

April 11, 2008

REVISION OF SECTION 411

EMULSIFIED ASPHALT

Section 411 of the Standard Specifications is hereby revised for this project as follows:

Subsection 411.02 shall include the following:

Emulsion used for cover coat will be identified as rapid setting or medium setting emulsion, and conform to the requirements of subsection 702.03

Subsection 411.04 shall include the following the following:

Emulsified asphalt used for seal coat will be measured by the actual number of tons placed and accepted.  The pay quantity of emulsified asphalt will be determined from the invoices of emulsified asphalt delivered to the project, corrected by any weight of remaining emulsion in the distributor truck or tanker at the conclusion of the project.  The Engineer may elect to calculate the remaining weight in a distributor by use of the average specific gravity of materials delivered, or by tank stabs.  The average specific gravity for this calculation will be as determined by Central Laboratory Testing.  If tank stabs are to be utilized for this measurement, the Contractor’s quality control plan shall include appropriate information for calculations on the distributor used on the project.  This calculation will be limited to 4000 gallons of material.  All other material shall require weigh back for proper calculation of payment.  The weight shall be determined by certified scales in accordance with Section 109.  This will also be monitored and documented by daily distributor gauge readings and yield calculations.  All proposed methods of weighing materials, calibrating distributor rates and monitoring the yields shall be included in the Quality Control Plan in accordance with Section 409.

Diluted emulsified asphalt used for fog coat in chip seals will be measured by the actual number of tons of asphalt prior to dilution with water. Correction for the final diluted emulsion at the conclusion of a project will assume a 3:2 emulsion to water dilution rate, and the water subtracted from the weight of the remaining product unless otherwise approved.

Subsection 411.05 shall include the following:

Pay Item													Pay Unit

Emulsified Asphalt (Rapid-Setting) (Polymerized)			Ton

Emulsified Asphalt (Medium-Setting) (Polymerized)			Ton

Water will not be measured and paid for separately but shall be included in the work.