September 2, 2005

REVISION OF SECTIONS 614 AND 630

FLASHING BEACON

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on projects that have flashing beacons or solar powered flashing beacons.

September 2, 2005

REVISION OF SECTIONS 614 AND 630

FLASHING BEACON

Sections 614 and 630 of the Standard Specifications are hereby revised for this project as follows:

Subsection 614.06 shall include the following:

614.06 Flashing Beacon.  Flashing beacon shall be as shown on the plans.  If solar power is called for on the plans, or if the Engineer approves the use of solar power, then the beacon head shall be 12V LED type operated at 24 watts. The solar power system shall be capable of operating the flashing beacon continuously for ten days without any sunlight. The solar panel and battery power system shall be augmented to protect it from vandalism or theft. The solar power system shall be complete including all elements required for an operational installation.

Subsection 614.09 shall include the following:

The flashing beacon shall be installed as shown on the plans. The solar power system shall be placed outside the clear zone of the roadway or behind guardrail. Batteries shall be placed in a lockable container attached to a supplemental pole supporting the solar panels that is installed outside the clear zone, or behind guardrail.

Subsection 614.13, twelfth paragraph, shall include the following:

Solar power system for flashing beacons, poles, and lockable container will not be measured and paid for separately, but shall be included in the work.

Subsection 630.08, third paragraph, shall include the following:

The flashing beacon shall be in accordance with subsection 614.06.

Subsection 630.12 shall include the following:

The flashing beacon shall be installed in accordance with subsection 614.09. For solar powered flashing beacons, batteries may be placed in a lockable container attached to a supplemental pole supporting the solar panels that is installed outside the clear zone, or behind guardrail. If it is not possible to place this assembly outside the clear zone or behind guardrail, the batteries shall be placed in a lockable pull box and buried at the base of the pole. Other installations shall be as approved.

The Contractor shall ensure the proper operation of the flashing beacon throughout the duration of the project.  If the beacon fails to operate properly, it shall be repaired or replaced at the Contractor’s expense.  The Contractor may propose an alternate method by submitting a revised MHT in accordance with subsection 630.09 for approval by the Engineer.  All additional traffic control devices required during the time that the beacon is being repaired or the MHT is being prepared and reviewed shall be at the Contractor’s expense.

Subsection 630.14, fourth paragraph, shall include the following:

Solar power system for Flashing Beacon (Portable), poles, and lockable container will not be measured and paid for separately, but shall be included in the work.