May 26, 2005

REVISION OF SECTION 630

CONSTRUCTION ZONE TRAFFIC CONTROL

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use this standard special provision on all projects.

Section 630 of the Standard Specifications is hereby revised for this project as follows:

Delete subsection 630.10 and replace with the following:

630.10 Traffic Control Management.  The Contractor shall designate an individual, other than the superintendent, to be the traffic control supervisor. The traffic control supervisor shall be certified as a worksite traffic supervisor by either the American Traffic Safety Services Association (ATSSA) or the Colorado Contractors Association (CCA), and shall have a current Department flagger’s certificate. A copy of the traffic control supervisor's certifications shall be provided to the Engineer at the preconstruction conference.

The Contractor’s Superintendent and all others serving in a similar supervisory capacity shall have completed a CDOT-approved two-day Traffic Control Supervisor training as offered by the CCA.  The one – day CCA Traffic Control Technician (TCT) training along with the two-day ATSSA Traffic Control Supervisor training will serve as an alternate. If the alternate is chosen, the Contractor shall provide written evidence that at least an 80 percent score was achieved in both of the two training classes.  The certifications of completion or certifications of achievement for all appropriate staff shall be submitted to the Engineer at the preconstruction conference.

The traffic control supervisor's duties shall include:

(1)	Preparing, revising, and implementing each required method of handling traffic in accordance with the traffic control plan.

(2)	Directly supervising project flaggers.

(3)	Coordinating all traffic control operations, including those of subcontractors and suppliers.

(4)	Coordinating project activities with appropriate police and fire control agencies.

(5)	Preparing a traffic control diary on every calendar day traffic control devices are in use. This diary shall be submitted to the Engineer daily and become a part of the Department's project records.  The diary shall include the following information as a minimum:

- Date

- For Traffic Control Inspection, the time of the inspection

- Project number

- Traffic Control Supervisor’s name

- Description of traffic control operations (lane closures, shoulder closures, pilot car operations, detours, etc.) including location, setup and takedown time, and approved method of handling traffic (MHT) number

- Types and quantities of traffic control devices used per approved MHT

- List of flaggers and uniformed traffic control (UTC) used, including start time, stop time, and number of flagging hours and UTC hours used

- Traffic control problems (traffic accidents; damaged, missing or dirty devices, etc.) and corrective action taken

(6)	Inspecting traffic control devices on every calendar day that traffic control devices are in use, masked, or turned away from traffic. These inspections shall include at least one night inspection per week.  The TCS or another representative who is certified as a work site traffic supervisor shall perform these inspections.

(7)	Insuring that traffic control devices are functioning as required.

(8)	Overseeing all requirements covered by the Contract which contribute to the convenience, safety and orderly movement of traffic. Have an up-to-date copy of the MUTCD and applicable standards and specifications available at all times on the project.

(9)	Attending all project scheduling meetings.

(10)	Supervising the cleaning and maintenance of all traffic control devices.

A certified worksite traffic supervisor shall provide traffic control management (TCM) on a 24-hour-per-day basis.  The traffic control supervisor (TCS) or another representative who is certified as a work site traffic supervisor shall be available and reasonably accessible to the job site on every working day, on call at all times, and available upon the Engineer's request at other than normal working hours. During non-work periods, the TCS or another representative shall respond to the job site within 45 minutes. When another representative responds, the TCS or another representative who is certified as a work site traffic supervisor shall arrive at the job site within two hours after notification.  The Contractor shall maintain a 24-hour telephone number at which the TCS can be contacted. The TCS shall not act as a flagger except in an emergency or in relief for short periods of time.

Delete subsection 630.14 and replace with the following:

630.14 Quantities to be measured for construction traffic control devices shall be the number of units of the various sizes and descriptions listed below.

Construction Traffic Signs:

Panel Size A:	Up to 1 m2 (0.01 to 9.00 Square Feet) including Type 1 and Type 2

Barricades.

Panel Size B:	Over 1 to 1.5 m2 (9.01 to 16.00 Square Feet)

Panel Size C:	Over 1.5 m2. (16.01 Square Feet and over)

Special: 		As shown on the plans

The total number of traffic control devices of each type on the schedule and approved subsequent modified schedules shall be the maximum number approved for payment.

Traffic channelizing devices consisting of vertical panel, traffic cones, or drum channelizing device will be measured by the unit. Concrete barriers will be measured by the meter (linear foot). Barricades will be measured by the number used. Barricade warning lights shall be furnished as a part of this item when required by the Traffic Control Plan (TCP). Advance Warning Flashing or Sequencing Arrow Panels will be measured by the unit according to size.

The flashing beacon (portable) will be measured as a unit complete in place. Sign panel will be paid for under the appropriate item.

The quantity to be measured for Traffic Control Management will be the number of authorized 24-hour  days of active TCM performed by the TCS or another representative certified as a work site   traffic supervisor.  Payment will be made for one day of Traffic Control Management regardless of the number of TCSs required to adequately control the work.  An authorized 24-hour day of active TCM will be every calendar day on which active traffic control occurs in accordance with an approved MHT.  This includes activities such as flagging operations, pilot car operations, and setting up or removal of construction zones, shoulder closures, lane closures or detours.  Traffic control devices that are left in place during non-working hours, including configurations such as lane closures, temporary channelization or detours, are not considered active traffic control.

The quantity to be measured for Traffic Control Inspection will be the number of authorized 24-hour days of traffic control inspection (TCI) performed by the TCS or another representative certified as a work site traffic supervisor.  An authorized 24-hour day of TCI shall be every calendar day that traffic control devices as shown in the MHT are in use, masked, or turned away from traffic on the project, and the only traffic control activity is the inspection of traffic control devices.

Resetting, repairing, or replacing traffic control devices is considered maintenance of the devices.  Cleaning and maintaining of traffic control devices are not considered traffic control activities subsidiary to the Traffic Control Management, Traffic Control Inspection or flagging pay items.

Payment will be made for either Traffic Control Management or Traffic Control Inspection for every calendar day that traffic control devices as shown in the MHT are in use, masked, or turned away from traffic on the project.  Payment will not be made for both items for the same calendar day.  Work on a night shift that begins before midnight and ends after midnight will be considered as occurring on the calendar day on which the shift ends.

The quantity to be measured for flagging will be the total number of actual flagging hours that are used as authorized in accordance with an approved MHT.  Payment will not be made for time spent by flaggers to set up and take dwon construction traffic control devices.  The quantity to be measured for pilot car operation will be the total number of hours that pilot car operation is used as authorized. Hours of flagging and hours of pilot car operation in excess of those authorized shall be at the Contractor's expense.

Delete subsection 630.15 and replace with the following:

630.15  Payment for the individual traffic control devices necessary to complete the work shall be full compensation for furnishing, erecting, cleaning, maintaining, resetting, repairing, replacing, moving, removing, and disposing of the construction traffic control devices. All construction traffic control devices that are not permanently incorporated into the project will remain the property of the Contractor.

Construction traffic control devices, as determined by the project traffic control plan (TCP), will be paid for as follows: 50 percent of the accepted amount upon first utilization, an additional 40 percent of the accepted amount when 75 percent of the original contract amount has been earned, and the final 10 percent when the project has been completed in accordance with subsection 105.16, exclusive of any maintenance periods.

The accepted quantities will be paid for at the contract unit price for each of the pay items listed below that appear in the bid schedule.

Payment will be made under:

Pay Item									Pay Unit

Construction Traffic Sign (Panel Size     )		Each

Construction Traffic Sign (Special)			Square Meter (Square Foot)

Vertical Panel								Each

Vertical Panel (With Light) (Flashing)			Each

Vertical Panel (With Light) (Steady Burn)		Each

Advance Warning Flashing

or Sequencing Arrow Panel (____Type)		Each

Drum Channelizing Device					Each

Traffic Cone								Each

Tubular Marker							Each

Channelizing Device (Fixed)					Each

Concrete Barrier (Temporary)				Meter (Linear Foot)

Delineator (Type    ) (Temporary)				Each

Barricade (Type     ) (Temporary)				Each

Traffic Control Management	 				Day

Traffic Control Inspection					Day

Flagging 									Hour

Pilot Car Operation		 					Hour

Flashing Beacon (Portable)					Each

Traffic Signal (Temporary)					Lump Sum

The Contractor shall agree to quantities for the following items on a weekly basis when signing the CDOT Form 7 – Weekly Report of Miscellaneous Pay Items:

Traffic Control Management	 				Day

Traffic Control Inspection					Day

Flagging 									Hour

Pilot Car Operation		 					Hour

Construction Traffic Sign (Special) is a project specific sign indicated on the Schedule of Construction Traffic Control Devices.

When Traffic Control Management and Traffic Control Inspection are not pay items, traffic control management will not be paid for separately, but shall be included in the work.

Flagger hand devices will not be measured and paid for separately, but shall be included in the work.

Cost of electrical power, including batteries, for all temporary lighting or warning devices shown on the TCP  will not be paid for separately but will be considered subsidiary to the item.

Temporary masking signs, including the covering materials and fastening devices, will not be measured and paid for separately but shall be included in the work.

The Contractor may provide larger construction traffic signs than those shown on the plans, if approved; however, payment will be made for the panel size designated.

If the Contractor fails to complete construction within the approved contract time, no payment will be made for the use of Section 630 pay items for the period of time after expiration of the approved contract time. These items shall be provided at the Contractor’s expense.

Cleaning and patching of the roadway after removal of the Channelizing Device (Fixed) will not be paid for separately, but shall be included in the work.