SSP Index 05-26-05

[For 1999 Spec Book]

COLORADO

DEPARTMENT OF TRANSPORTATION

SPECIAL PROVISIONS

▀{Project Location}

STANDARD SPECIAL PROVISIONS

Date	No. of Pages

Revision of Section 101-Holidays	(May 31, 2001)	1

All projects.

Revision of Section 101 – Pavement Structure and Subgrade	(April 1, 2004)	1

All projects.

Revision of Sections 101 and 105 – Duties of the Engineer	(Nov. 5, 1999)	1

All projects.

Revision of Sections 101 and 108 – Workplace Violence	(March 15, 2002)	1

All projects.

Revision of Section 103 – Colorado Resident Bid Preference	(July 21, 1999)	1

Projects funded without federal aid.

Revision of Section 103 – Contract Bonds	(Nov. 5, 1999)	1

All projects.

Revision of Section 103 – Escrow of Proposal Documentation	(July 21, 1999)	3

# Projects approved by the Region Transportation Director that meet the following

# criteria:

# Complex projects with contract amount greater than $3 million and tunneling work,

# overlap of or proximity to projects that could result in conflicts,

# complex state of the art structures, high risk of encountering hazardous materials,

# entity, government agency, or private agency involvement.

Revision of Section 104 – Value Engineering Change Proposals	(May 26, 2005)	5

All projects.

Revision of Section 105 – Conformity with Plans and Specifications	(May 26, 2005)	5

All projects.

Revision of Section 105 – Disputes and Claims for Contract Adjustments	(Oct. 14, 2003)	12

All projects.

Revision of Section 105 – Violation of Working Time Limitation	(July 21, 1999)	1

Projects that have a working time limitation specified in the project special provisions.

Revision of Sections 105 and 106 – Quality of Hot Bituminous Pavement	(March 18, 2005)	11

Projects with 5000 or more tons of HBP when acceptance is based on gradation, asphalt content, and in-place density.

Note: This specification requires a Force Account item for incentive payment.

Revision of Sections 105 and 106 – Quality of Hot Bituminous Pavement

(Less than 5000 Tons)	(Oct. 14, 2003)	6

Projects with less than 5000 tons of HBP.

Note: This specification requires a Force Account item for incentive payment.

Revision of Sections 105 and 106 – Quality of Hot Bituminous Pavement

(Voids Acceptance)	(Jan. 16, 2004)	10

Projects with 5000 or more tons of HBP when acceptance is based on asphalt content, voids in the mineral aggregate, air voids, and in-place density.

Note: This specification requires a Force Account item for incentive payment.

Revision of Sections 105, 106, and 412 – Quality of Portland Cement Concrete

Pavement (Alternative Strength Criteria)	(March 11, 2004)	11

Appropriate projects with portland cement concrete pavement having more than 5,000 square yards of paving as determined by the Region where acceptance will be based on either compressive strength criteria or flexural strength criteria as selected by the Contractor.

Note: This specification requires a Force Account item for incentive payment.

Revision of Sections 105, 106, and 412 – Quality of Portland Cement Concrete

Pavement (Compressive Strength Criteria)	(March 11, 2004)	7

Appropriate projects with portland cement concrete pavement as determined by the Region where acceptance will be based on compressive strength criteria.

Note: This specification requires a Force Account item for incentive payment.

Revision of Sections 105, 202, 401, 405, 406, and 412 – Roadway Smoothness	(Oct. 14, 2003)	10

Projects that have plant mix pavement construction, portland cement concrete pavement construction, one of the intermediate treatments listed in subsection 105.031(c), or any combination thereof.

Note: This specification requires a Force Account item for incentive payment.

Note: The Engineer should specify the the pavement smoothness category and either inches/mile or percent improvement in the plans.

Revision of Sections 105 and 618 – Contractor Submittals		(March 18, 2005)	   	1

All Projects.

Revision of Section 106 – Certificates of Compliance and Certified Test Reports	(March 18, 2005)	2

All Projects.

Revision of Sections 106 and 620 – Qualification of Testing Personnel and Laboratories   (Oct. 4, 2001)	1

All Projects.

Revision of Section 107 – Project Safety Planning	(May 26, 2005)	3

All projects.

Revision of Section 107 – Responsibility for Damage Claims, Insurance Types

and Coverage Limits	(May 26, 2005)	2

All Projects.

Revisions of Sections 107 and 412 – Concrete Wastewater Containment                            (March 11, 2004)	1

Projects having any type of concrete construction.

Revision of Section 108 – Liquidated Damages	(June 13, 2003)	1

All Projects.

Revision of Section 108 – Notice to Proceed	(Dec. 20, 2002)	1

All Projects.

Revision of Section 108 – Payment Schedule	(July 24, 2000)	1

Seventh Pot Projects.

Revision of Section 108 – Project Schedule	(March 4, 2002)	2

All projects.

Revision of Section 108 – Subletting of Contract	(Sept. 6, 2002)	1

All projects.

Revision of Section 109 - Adjustments for Changes in Common Carrier Rates	(May 31, 2001)	1

Projects having asphalt pavement or bituminous materials pay items.

Revision of Section 109 - Fuel Cost Adjustments	(May 31, 2001)	1

Projects with contract times longer than 1 year.

Note: This specification requires a Force Account item.

Revision of Section 109 – Measurement of Quantities	(July 21, 1999)	1

Federal aid projects.

Revision of Section 109 – Retainage and Partial Payments	(August 26, 2004)	2

All Projects.

Revision of Section 203 - Proof Rolling	(March 4, 2002)	1

Projects requiring compaction to the subgrade.

Revision of Section 206 – Shoring 	(July 18, 2003)	2

Projects having pay item 206, Shoring (Area__ ) on the Bridge plan sheets.

Revision of Section 208 – Erosion Control	(March 11, 2004)	4

Projects subject to an NPDES Permit, and projects that include any of the erosion control work identified in subsection 208.04.  Do not use on projects, such as overlay projects, that have no earth disturbance other than minor shouldering work, unless the disturbed earth is expected to be subject to significant erosion.

Revision of Section 208 – Erosion Control Supervisor	(March 6, 2003)	1

Projects with any type of erosion control work.

Revision of Section 208 – Stabilized Construction Entrance	(March 11, 2004)	1

Projects having stabilized construction entrances as part of erosion control measures.

Revision of Section 209 - Dust Palliatives	(May 31, 2001)	1

All projects.

Revision of Section 307 - Lime Treated Subgrade	(August 26, 2004)	6

Projects having lime treated subgrade.

Revision of Section 401 – Bituminous Paver	(Jan. 16, 2004)	1

Projects having hot bituminous pavement.

Revision of Section 401 – Compaction Test Section	(Sept. 6, 2002)	3

Projects having hot bituminous pavement.

Revision of Section 401 – Composition of Mixtures	(June 24, 2004)	4

Projects having hot bituminous pavement.

Revision of Section 401 – Plant Mix Pavements	(July 21, 1999)	1

Projects as determined by the Region.

Revision of Section 401 – Plant Mix Pavements - General	(Oct. 14, 2003)	3

Projects with any grading of hot bituminous pavement.

Revision of Section 401 – Reclaimed Asphalt Pavement	(Oct. 14, 2003)	2

Projects with voids acceptance of hot bituminous pavement, and on any other projects

as determined by the Region Materials Engineer.

Revision of Section 401 – Tolerances for Hot Bituminous Pavement  (Voids Acceptance) (July 21, 1999)	1

Projects with HBP when acceptance is based on asphalt content, voids in the mineral aggregate, air voids, and in-place density.

Revision of Section 401 – Weather Limitations and Placement Temperatures	(March 4, 2002)	2

Projects with any grading of HBP.

Revision of Section 411 – Bituminous Materials	(May 26, 2005)	1

Projects having emulsified asphalt used for seal coat and fog coat in chips seals.

Revision of Section 412 – Construction Joints	(June 24, 2004)	2

Projects having portland cement concrete pavement

Revision of Section 412 – Portland Cement Concrete Pavement	(March 18, 2005)	6

Projects with concrete paving items.

Revision of Sections 412 and 705 – Preformed Compression Seals	(July 21, 1999)	2

Projects where it is necessary to use preformed compression seals in lieu of silicone sealant in concrete pavement joints, such as projects with fast track concrete.

Revision of Section 509 – Erection of Structures	(August 9, 2004)	1

Projects having steel structures and structural steel members.

Revision of Section 509 – Stud Welding	(March 4, 2002)	1

Projects having shear connectors.

Revision of Section 512 – Bearing Devices	(June 13, 2003)	1

Projects requiring bearing devices.

Revision of Section 601 – Concrete Construction Tolerances 	(Oct. 14, 2003)	1

Projects having concrete structures.

Revision of Section 601 – Structural Concrete	(June 13, 2003)	13

Projects having any type of concrete construction.

Revision of Sections of 601 and 618 – Permanent Bridge Deck Forms 	(July 18, 2003)	2

Projects having permanent bridge deck forms.

Revision of Sections 601 and 708 – Structural Concrete Coating	(July 21, 1999)	3

Projects that include structural concrete coating.

Revision of Section 602 – Installation of Tie Wire	(March 4, 2002)	1

Projects having reinforcing steel.

Revision of Section 606 - Guardrail Terminals and Transitions	(May 31, 2001)	1

Projects having Guardrail Type 3 W Beam.

Revision of Section 606 – Guardrail Type 7 (F-Shape Concrete Barrier)	(July 2, 2002)	2

Projects having concrete barrier.

Revision of Section 606 – Precast Type 7 Concrete Barrier	(July 2, 2002)	1

Projects having concrete barrier.

Revision of Section 613 – Screw-In Light Standard Foundations	(July 21, 1999)	2

Projects where one or more 40 foot (12.2 m) light standards are to be installed.

Revision of Section 614 – Sign Illumination and Illuminated Signs	(June 13, 2003)	1

Projects having illuminated signs.

Revision of Section 614 - Traffic Signal Poles	(May 31, 2001)	1

Projects having traffic signal poles.

Revision of Sections 614 and 630 – Retroreflective Sign Sheeting	(August 26, 2004)	1

All Projects.

Revision of Section 618 – Erection of Structures	(August 9, 2004)	1

Projects having prestressed concrete members.

Revision of Section 618 – Grouting of Post Tension Ducts	(July 18, 2003)	5

Projects having post tensioning ducts.

Revision of Section 618 – Steel Diaphragms	(August 26, 2004)	1

Projects having precast, prestressed concrete girders.

Revision of Section 620 – Field Laboratories with Forced Air Convection Oven	(March 6, 2003)	3

Projects having 5000 or more tons of HBP and requiring a Contractor furnished field laboratory with a forced air convection oven.

Revision of Section 620 – Field Laboratories without Forced Air Convection Oven	(March 6, 2003)	2

Projects with less than 5000 tons of HBP and requiring a Contractor furnished field laboratory; and projects with 5000 or more tons of HBP and requiring a Contractor furnished field laboratory without a forced air convection oven.

Revision of Sections 627 and 713 – Preformed Plastic Pavement Marking	(May 26, 2005)	2

Projects having Preformed Plastic Pavement Marking.

Note: Designer should specify Pavement Marking Type and Class in the plans and should indicate whether Pavement Marking should be inlaid or placed directly on to roadway surface.  Designer should contact the Region Traffic Engineer for more information.

Revision of Section 629 – Survey Monumentation	(Dec. 20, 2002)	1

Projects having Survey Controls.

Revision of Section 630 – Construction Zone Traffic Control	(May 26. 2005)	4

All projects.

Revision of Section 630 – Method of Handling Traffic	(Oct. 14, 2003)	1

All projects.

Revision of Section 630 – NCHRP 350 Requirements	(August 26, 2004)	1

All projects.

Revision of Section 630 – Portable Sign Storage	(May 26, 2005)	1

All projects.

Revision of Section 630 – Signing for Double Fines	(June 13, 2003)	1

Projects requiring double fine and reduced speed limit signs.

Section 641 – Shotcrete	(March 18, 2005)	5

Projects having Shotcrete.

Revision of Section 701 – Hydraulic Cement	(March 6, 2003)	2

All projects having any type of concrete construction.

Revision of Section 702 – Asphalt Emulsions	(May 26, 2005)	3

Projects with pay items from sections 405, 406, 407,409, and 41l.

Revision of Section 702 – SuperPave PG Binders	(May 26, 2005) 	2

Projects with HBP with Superpave performance graded binders.

Revision of Section 703 – Aggregate for Plant Mix Pavements	(Oct. 14, 2003) 	2

Projects having hot bituminous pavement or stone mastic asphalt (SMA).

Revision of Section 703 – Concrete Aggregates	(March 6, 2003) 	1

Projects having any type of concrete construction.

Revision of Section 706 – Concrete Pipes	(Dec. 20, 2001)	1

Projects with concrete pipes or in which concrete pipes are an allowable option.

Revision of Section 712 - Plastic Pipe	(Dec. 20, 2002)	1

Projects having culvert pipe.

Revision of Section 712 - Riprap for Slope Mattresses	(May 31, 2001)	1

Projects having slope mattresses.

Revision of Section 713 – Epoxy Pavement Marking Material	(June 8, 2000)	1

Projects with epoxy pavement marking.

Affirmative Action Requirements – Equal Employment Opportunity	(July 21, 1999)	10

All projects.

Disadvantaged Business Enterprise – Definitions and Requirements	(August 26, 2004)	11

All projects.

Emerging Small Business Program	(March 15, 2002)	8

All projects that are not partially or wholly  funded with local agency funds.

Note: For projects having construction budgets less than $1 million, the designer shall include $5,000 for the Emerging Small Business (ESB) Force Account Item.  For projects having construction budgets greater than $1 million, the ESB Force Account Item shall have an amount of $7,500.

Materials and Labor Used, Form FHWA-47	(July 21, 1999)	1

Federal aid projects on the National Highway System that will or might have a total final construction cost of $1 million or more.

Minimum Wages Colorado,

U.S. Department of Labor General Decision Numbers CO030014 and CO030015,

MOD 11, Highway Construction, Statewide	(May 6, 2005)	9

Federal aid projects exceeding $2000 and all related subcontracts, except for projects on roadways classified as local roads or rural minor collectors, which are exempt.

On the Job Training	(Dec. 20, 2002)	4

All Projects.

Note:  The designer shall use the appropriate OJT Colorado Training Program estimate amount from the following table for the OJT Colorado Training Program Force Account Pay Item:

| Project Construction Budget | OJT Colorado Training Program |
| --- | --- |
| Below $50,000 | $0.00 |
| $50,000 - $99,999 | $100.00 |
| $100,000 - $249,999 | $150.00 |
| $250,000 - $499,999 | $200.00 |
| $500,000 - $999,999 | $300.00 |
| $1,000,000 - $2,249,999 | $525.00 |
| $2,250,000 - $4,999,999 | $1,000.00 |
| $5,000,000 – $9,999,999 | $2,100.00 |
| $10,000,000 – $19,999,999 | $5,250.00 |
| $20,000,000 – $49,999,999 | $9,000.00 |

In addition, additional funding shall be included for the number of hours of OJT Training that is required as a separate force account.  Please contact the Region EO Office for details.

Partnering Program	(July 21, 1999)	1

Projects selected by the Region that meet the following guidelines:

Estimated contract amount of $3 million or more, or  projects that have one or more of the following elements: tunneling work, overlapping or close proximity projects that could result in conflicts, complex state of the art structures, high risk of encountering hazardous materials, entity, local government agency, or private agency involvement, utility relocations to be coordinated with construction, or construction under heavy traffic with construction phasing.

Railroad Insurance	(July 21, 1999)	1

Projects that require railroad insurance.

Required Contract Provisions – Federal-Aid Construction Contracts	(July 21, 1999)	11

Federal aid projects.

Special Notice to Contractors	(May 26, 2005)	4

All projects.

## INSTRUCTIONS TO DESIGNERS (delete these instructions and the instructions that follow each listed standard special provision from the final draft):

▀	Type in the project location here.

The above is a complete list of standard special provisions.  Each standard special provision is followed by an instruction on its appropriate use.  Each instruction can be interpreted by the words “Use on…”.  (For example: “Use on All projects”.)  For complete instructions on the use of a standard special provision, refer to the transmittal letter with the same date as the standard special provision.  Use only those standard special provisions applicable to the project.  Delete from the final draft the listings of standard special provisions which do not apply to the project.