FUEL COST ADJUSTMENT

This Construction Bulletin will assist with the implementation and interpretation of the Revision of Section 109 – Fuel Cost Adjustment standard special provision, dated November 14, 2005.  Subsection 109.6.4 is hereby added to the Construction Manual:

109.6.4 Fuel Cost Adjustment

The standard special provision at: http://www.dot.state.co.us/DesignSupport/Construction/2005SpecsBook/2005index.htm  will now be used on every project.  Contractors are allowed to “opt-in” (accept) or “opt-out” (not accept) Fuel Cost Adjustments by checking one of two blank lines on the Form 85, “Contractor’s Proposal”.  They are required to turn in the Form 85 at the time they submit their bids.  Contractors are not allowed to change their minds regarding Fuel Cost Adjustments after bids are opened.

After the Resident Engineer receives a copy of the executed Contract from Contracts and Market Analysis, he or she must notify the Project Engineer whether or not to make Fuel Cost Adjustments.

If the Contract contained one of the earlier versions of the standard special provision (dated August 1, 2005 for the new Blue spec book or May 31, 2001 for the Purple spec book), that standard special provision should continue to be used.  This new standard special provision will only apply to new Contracts.

No retroactive Fuel Cost Adjustments will be allowed.  In other words, this standard special provision should not be applied or change-ordered into any Contract that did not contain it at the time of bid opening.

No Fuel Cost Adjustment should be made to any item besides those shown in the specification.  Fuel Cost Adjustments will only be made to earthwork, Aggregate Base Course, Hot Mix Asphalt, and Portland Cement Concrete Pavement items.

If the Contractor accepted Fuel Cost Adjustments, the Project Engineer should calculate the adjustments once per month using the spreadsheet at: http://www.dot.state.co.us/DesignSupport/Construction/Fuel%20Cost%20Adjustments/Fuel%20cost%20adjustment%202.xls .  The spreadsheet contains additional detailed instructions regarding Fuel Cost Adjustments.  If you have questions, please contact Randy Furst in Project Development at 303-757-9233.