December 8, 2005

REVISION OF SECTION 105

CONFORMITY TO ROADWAY SMOOTHNESS CRITERIA

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies that use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use only on projects requiring smoothness testing by the profilograph method in which the Region Materials Engineer calls for its use.

December 8, 2005

REVISION OF SECTION 105

CONFORMITY TO ROADWAY SMOOTHNESS CRITERIA

Section 105 of the Standard Specifications is hereby revised for this project as follows:

In subsection 105.07 delete Table 105-8 and replace with the following:

# TABLE 105-8

PI FOR NO DISINCENTIVE OR CORRECTIVE WORK

FOR % IMPROVEMENT (%I)

| PAVEMENT SMOOTHNESS CATEGORY | DESCRIPTION | PI |
| --- | --- | --- |
| I | Rural Interstate | 16 inches/mile |
| II | All other highways with speed limits greater than or equal to 45 MPH | 18 inches/mile |
| III | All highways with speed limits less than 45 MPH | 20 inches/mile |

Delete 105.07 (c) and replace with the following

(c)	Smoothness Requirements for the work items: Removal of Asphalt Mat (Planing), Heating and Scarifying, Cold Bituminous Pavement Recycle, Heating and Repaving, and Heater Remixing.

1.	Testing procedures. A Profile Index (PI) for each 0.1 mile section shall be determined on the original pavement surface prior to beginning the work, using a 0.1 inch blanking band in accordance with CP 70.

A Profile Index (PI) for each 0.1 mile section shall be determined on the pavement surface after the work is complete using a 0.1 inch blanking band.

- Final pavement smoothness acceptance will be made as follows:

When 0.1 mile section has a final Profile Index (PI) greater than 18 in/mile and the final PI is greater than the PI prior to performing the work, that 0.1 mile section shall be corrected by a method approved in writing by the Engineer.  Corrective work shall be such that the resulting final PI is equal to or less than the initial PI or 18 in/mile.  All corrective work shall be at the Contractor’s expense, and shall include traffic control, and all additional hot mix asphalt required.