Department of Transportation

Project Development Branch

Standards and Specifications Unit

4201 East Arkansas Avenue, Room 290

Denver, Colorado  80222

(303) 757-9040  FAX:(303)757-9820

MemoranduM

DATE:		January 28, 2010

TO:		All Holders of Standard Special Provisions

FROM:		Larry Brinck, Standards and Specifications Engineer,

Project Development Branch

SUBJECT:	Revision of Sections 105, 202, 401, 406, and 601, Hot Mix Asphalt Pavement Roadway Smoothness (High Speed Profiler)

As of this date, our unit is issuing a revised version of the standard special provision, Revision of Sections 105, 202, 401, 406, and 601, Hot Mix Asphalt Pavement Roadway Smoothness (High Speed Profiler).  This new standard special is 9 pages long and is dated January 28, 2010.  Use this standard special in projects having hot mix asphalt.  This standard special will be required in projects that are advertised on or after February 25, 2010.  But, feel free to use this standard special before this date.

This revised standard special provision replaces one having the same name, dated November 5, 2009.  The following are modifications contained in this revised version:

- Doubling of incentive/disincentive for pavement smoothness based on inches per mile

- Corrective work can no longer be performed prior to smoothness acceptance testing

- Coring requirements to confirm maintenance of the minimum thickness have been defined

- Minor updates

Those of you who keep books of standard special provisions should replace the obsolete version of this standard special provision with this one.  A new index of Standard Special Provisions, dated January 28, 2010, is attached.

mrs/lb

Attachment

Distribution: Per Distribution List