January 28, 2010

REVISION OF SECTION 627

PAVEMENT MARKING

NOTICE

This is a standard special provision that revises or modifies CDOT’s Standard Specifications for Road and Bridge Construction  It has gone through a formal review and approval process and has been issued by CDOT’s Project Development Branch with formal instructions for its use on CDOT construction projects.  It is to be used as written without change.  Do not use modified versions of this special provision on CDOT construction projects, and do not use this special provision on CDOT projects in a manner other than that specified in the instructions unless such use is first approved by CDOT’s Standards and Specifications Unit.  The instructions for use on CDOT construction projects appear below.

Other agencies which use the Standard Specifications for Road and Bridge Construction to administer construction projects may use this special provision as appropriate and at their own risk.

Instructions for use on CDOT construction projects:

Use in projects having pavement marking.

Section 627 of the Standard Specifications is hereby revised for this project as follows:

Delete subsection 627.03(b) and replace with the following:

(b)	Roadways Closed to Traffic During Construction.  Full-compliance final markings shall be in place prior to opening the roadway to traffic.

Pavement markings on detour routes shall be full-compliance markings.

Delete subsections 627.03(d) and 627.03(e) and replace with the following:

(d)	Temporary Pavement Markings. Temporary pavement markings and control points for the installation of those pavement markings for roadways that are being constructed under traffic shall be installed as follows:

- When one roadway of a normally physically divided highway is closed, and a crossover is constructed, full-compliance pavement markings shall be placed along the tapers and through the median crossovers to the two-way traffic section.  Pavement markings through the two-way traffic section shall be as shown on the plans.

All temporary paved roadways shall have full-compliance center line, lane line, and edge line markings before they are open for traffic.

Upon removal, markings applied to a final surface shall not leave a scar that conflicts with permanent markings.

- The following criteria apply to all construction on roadways open to traffic other than (d)1. above:

Full-compliance center line, lane line, and edge line temporary markings shall be in place at the end of each work day.

No-passing zone restrictions shall be identified by full-compliance no-passing zone markings. No-passing zone markings shall be in place daily.

Temporary pavement stencils (SCHOOL, RR xing, etc) are not required unless specified in the plans.

Temporary pavement markings shall be installed according to the manufacturer’s recommendations in such a way that the markings adequately follow the desired alignment.

3.	Control Points consisting of 4 inch by 1 foot marks at 40-foot intervals may be placed as guide markers for the installation of temporary or final pavement markings. Raised flexible pavement markers may be substituted for these marks.  Control points shall not be used as a substitute for any required marking.

(e)	Pavement Marking for Seal Coats (Section 409).

1.	Raised flexible pavement markers, suitable for use on seal coats, shall be installed as follows:

No-passing zones shall be marked with two markers placed side-by-side at 40-foot intervals throughout the zone.

Passing zones shall be marked with one marker at 40-foot centers. Closer spacing shall be used on curves, as deemed appropriate.

Raised flexible pavement markers, installed on 40-foot centers, may also be used to mark lane lines through multi-lane roadway sections.  Auxiliary lanes and shoulder lines may be marked with flexible markers on 80-foot centers or as appropriate.

2.	Full-compliance final pavement markings shall be placed within one week of completion of the seal coat project.

In subsection 627.04, delete the second paragraph and replace with the following:

Equipment shall have a bead dispenser directly behind, synchronized with the paint applicator and shall be capable of painting a clean-edged stripe of the designated width ± ¼ inch with no overspray on the road surface. For centerlines and lane lines, an automatic skip control shall be used.  Machines having multiple applicators shall be used for centerlines with “no passing zones.” In areas where machines are not practical, suitable hand-operated equipment shall be used as directed by the Engineer. Stripes shall be protected until dry.

Subsection 627.13 shall include the following:

Each authorized application of temporary pavement marking will be measured and paid for at the contract unit price for the type of material used.

Control points and Contractor pavement marking plans will not be measured and paid for separately, but shall be included in the work.